## Slide 1: Application of Hyperspectral Sensors in Agricultural Monitoring System
Group: Hyperspectral
Group Leader
Afroza Begum
Group Members
01. Mohammad Monirul Hasan Tipu
02. Suman Biswas
03. Marina Afroze
04. Md Asaduzzaman
05. AFM Ruhul Quddus
06. Md. Mosiur Rahman Bhuyin Apu
07. Ummy Kulsum Mukta

## Slide 2: Hyperspectral Sensors
Hyperspectral remote sensing combines imaging and spectroscopy in a single system which often includes large data sets and require new processing methods.
Hyperspectral sensors capture energy in a large number of adjacent bands which means that they continuously cover the reflecting spectrum for each pixel in the scene.
Hyperspectral image is collected as a data cube with spatial information.
Fig. Hyperspectral image

## Slide 3
Characteristics of hyper-spectral sensors
Hyperspectral data sets are generally composed of about 100 to 1000 spectral bands of relatively narrow bandwidths (5-20 nm) that are found in the electromagnetic spectrum from visible, near infrared, medium infrared to thermal infrared. In general, they don’t have descriptive channel names.
Hyperspectral imagery is typically collected (and represented) as a data cube with spatial information collected in the X-Y plane, and spectral information represented in the Z-direction.

## Slide 4: Types of Hyperspectral Imaging
Hyperspectral cameras can capture information in four ways:
  Whiskbroom (point scanning) cameras
  Pushbroom (line scanning) cameras
  Cameras based on spectral scanning (area scanning or plane scanning)
  Snapshot (single shot) cameras.

## Slide 5: Types of Hyperspectral Sensors
Based on operational modes, there are 03 types of hyperspectral sensors:
Operation Modes | Spectral Range (nm) | Types of Sensors
Ground Based | 400-2500 | 01. Vehicle Mounted 02. Laboratory Measurement 03. Hand-held Mounted
Air borne | 380-12700 | AVIRIS HYDICE PROBE-1 CASI HyMap EPS-H DAIS 7915 DAIS 21115 AISA
Space borne | 400-14400 | FTHSI on MightySat II Hyperion on EO-1

## Slide 6
Vehicle Mounted
Ground-Based
Operational Modes
Reception of the vast volumes of HS data
Handheld Mounted
For close-range HS data from 8 to 12μ
Assist in material characterization
Air borne
Space Borne
Laboratory Measurement
For in situ ground spectral measurements
the detection and recognition steps yield accompanying spectral features
time-saving and facilitates the employment of less-qualified decoding personnel
Can get high spatial and spectral resolution simultaneously
Types of Hyperspectral Narrowband

## Slide 7
Sensor name | Band Number | Wavelength (µm) | Bandwidth (µm) | Spatial Resolution (m) | Radiometric Resolution | Swath wide (Km) | Revisit Time (Days) | Satellite name
FLORIS | 300 | 0.5-0.78 | - | 300 |  | 150 | - | FLEX
GEMS | 250 | 0.32-0.05 | 0.0008 | 7000 |  | - | - | GEO-KOMPSAT-2B
HSI | 232 | 0.42-2.45 | - | 30 |  | 30 | - | EnMAP
Hyperion | 220 | 0.4-2.5 | 0.01 | 30 | 16 bits | 7.5 | 16 days | EO-1
HysIS | 316 | 0.4-2.4 | 0.01 | 30 |  | 30 | - | HysIS
PRISMA | 240 | 0.42-2.5 | 0.01-0.3 | 5-30 |  | 30 | 6 | PRISMA
IRS | 1720 | 4.6-14.3 | - | 4000 |  | - | 0.04166 | MTG-S1, MTG-S2
OCIOCI (on PACE) | - | 0.34-2.26 | - | 1000 |  | - | 2 | PACE
TEMPO | 666 | 0.29-0.74 | 0.0002 | 4400 |  | - | - | TEMPO
UVN (Sentinel-4) | 598 | 0.31-0.78 | 0.00012-0.005 | 8000 |  | - | 0.04166 | MTG-S1, MTG-S2
UVNS (Sentinel-5) | 3936 | 0.27-2.39 | 0.00025-0.001 | 7000-28000 |  | 2715 | 1 | MetOp-SG A1, Metop-SG A2, Metop-SG A3
IASI-NG | 16921 | 3.62-50.5 | - | 25000 |  | 2130 | - | same
AVIRIS | 224 | 0.4-2.5 |  | 20 |  | 12 |  | ER-2
Characteristics of different Hyper-spectral sensors
Source: ITC

## Slide 8
Fig: Flow-chart of the application of different pre-processing steps. The red arrow indicate ideal path. The blue arrow indicate a possibility when background removal is the main critical step and is perform manually.
There is not a correct or logical order to perform image pre-processing. Choose the correct pre-processing steps highly depends on the difficulty of the data, the quality of the images, the availability of methods, the target of the analysis and the priority in the data acquisition.
Pre-processing

## Slide 9
Methods | Purpose | Source
Supervised image classification (CNN, ANN, SVM, KNN, SAM etc.) | -To representing particular ground cover types, or classes, mapping the land use/cover -Pesticide residue monitoring -detecting burnt areas in a typical Mediterranean setting -Quality grading of fruits - Defect detection -Chilling injury | Jiaji Zhu et. al. (2021) Konstantinos et. al. (2013) Rendong et. al. (2021)
Hyperspectral Narrowband Indices |  | 
Hyperspectral Vegetation Index (HVI) | Structure (properties such as biomass, leaf area index, or fraction of photosynthetically active radiation) | Gitelson et al. (1996)
Hypersepctral Normalized Difference Vegetation Index (HNDVI) | Structure | Oppelt and Mauser (2004)
Greenness Index (GI) | Structure | Zarco-Tejada et al. (2005)
Hyperspectral Normalized Difference Water Index (HNDWI) | Water (leaf water content) | Gao (1996)
Normalized Difference Infrared Index (NDII) | Water | Hardisky et al. (1983)
Water Index(WI) | Water | Penuelas et al. (1997)
Photochemical Reflectance Index (PRI) | Physiology (properties related to stress such as light-use efficiency or red-edge) | Gamon et al. (1992)
Red-Edge Vegetation Stress Index (RVSI) | Physiology | Merton and Huntington (1999)
Modified Chlorophyll Absorption Ratio Index (MCARI) | Physiology | Daughtry et al. (2000)
Remote Sensing Methods
Ref.: Marshall et. al. 2015

## Slide 10: Application of Hyperspectral data
Hyperspectral data offer the possibility to retrieve biochemicals via specific pigments such as chlorophyll, anthocyanins or carotenoids, and thus give farmers access to primary production, pest and disease monitoring.
Hyperspectral data allow discriminating the absorptions of atmospheric water vapor from those of cellulose and lignin to quantify non-photosynthetic vegetation and thus give farmers access to improved crop residue management.
Hyperspectral data support the discrimination of the three phases of water (ice, liquid, gas) and thus give farmers access to plant water status monitoring.
Hyperspectral data can help to discriminate protein absorptions from the overlaying cellulose, lignin and water absorptions and thus give farmers access to improved fertilization efficiency monitoring.

## Slide 11
Hyperspectral Imaging
Precision Agriculture
Vegetative cover
Ecological Monitoring
Environmental monitoring
Yield Estimation
Crop stress-(nutrients, water, disease, pests)
Soil characterization
Food quality and contamination
Crop Classification

## Slide 12: Advantages of imaging spectroscopy for agriculture
Higher accuracy of variable retrieval
Improved automatic interpretation of EO signals by spectrally separating atmosphere, soil, leaves and canopy effects, since ambiguities are reduced
Higher accuracy of crop species discrimination
Novel approaches that provide access to variables hidden for multispectral sensors, e.g., Sun induced chlorophyll inflorescence

## Slide 13
Advantages of Hyperspectral Versus others Sensing in an Agricultural Context
Hyperspectral image give spectrally continuous sampling i.e. high spectral resolution
Hyperspectral approaches have contributed largely in precision agriculture.
An increase in agricultural crop species classification accuracy (some literature stated about 43%) is observed.
Crop discrimination can be traced through hyperspectral sensing.
Following the “one key fits all” principle, a hyperspectral sensor can easily serve different applications.

## Slide 14: Limitations
The rare availability of spaceborne hyperspectral sensors
The construction of hyperspectral sensors compared to multispectral instruments is complicated as well as expensive
High spectral dimensionality is provided by hyperspectral sensors resulting long processing times
Hyperspectral algorithm development for vegetation studies so far has been mostly limited to airborne data, which is very heterogeneous in quality, temporal availability and spatial coverage.

## Slide 15: Challenges
Lack of homogenous crop farming i.e. crops that form geometrically homogeneous stands compared to the observation scale of spaceborne sensors and which are cultivated in areas with individual field sizes in the order of 1 hectare and above.
Smallholder farming, which still is practiced on about 12% of global farmland probably will most likely not be able to adapt the new technologies in near future.
Farmers need to be convinced

## Slide 16: Future directions
Introduce global satellite mission based on dedicated acquisition plan
Installing different instruments along one orbit to follow each other in a so-called train constellation would be a sensible strategy, allowing the integration of new technologies into the chain as they become available
To exploit the full potential of multi angular observations, a tandem concept of two identical instruments in parallel fight could be envisioned.
The increased data rates expected with high-resolution spectroscopy missions will pose new challenges for efficient data downlinking, data storage and data distribution. Advanced on board processing strategies should be developed to mitigate the data rate problems.

## Slide 17
Analytical method
Timesat
(A software package to analyse time-series of satellite sensor data)
Application:
-Estimating growing seasons from satellite time-series
-Computing phenological metrics (beginning and end of the growing season, length of the season, amplitude, integrated value, asymmetry of the season etc.) from the data.
-Mapping environmental and phenological changes as well as ecosystem classification
-Using in Terra/MODIS data in the development of systems for detection of forest disturbances, e.g. due to insect infestations
(Jönsson and Eklundh 2002, 2003, 2004, Eklundh and Jönsson 2003).

## Slide 18
Advantages:
-Have good performance, balancing the ability to reduce noise and the maintenance of signal integrity.
Disadvantage:
-The current TIMESAT version is based on data values that are equally spaced in time.
-Since many data products, such as MODIS NDVI or EVI composites, are composed of data from irregularly spaced observation dates, this may lead to errors in the timing of seasonal profiles and phenological parameters.