## Slide 1
Exploring Multispectral and Thermal Sensors regarding its application in Agricultural Monitoring System
Group Name: ‘Multispectral Broadband + Thermal’ group
Coordinator: Dr. Taslima Zahan
Group: Multispectral Broadband | Group: Thermal band
1. Dr. Md. Golam Mahboob, SSO, ASICT Division, BARI | 1. Shakhawat Hossain, RA, Agro-Environmental Remote Sensing and Modeling Lab, ASICT Division, BARI
2. Dr. Taslima Zahan, SO, OFRD, BARI | 2. Dr. AFM Tariqul Islam, SSO, ASICT Division, BARI
3. Mustafa Kamal Shahadat, SO, OFRD, BARI | 3. Istiak Ahmed, SO, ASICT Division, BARI
4. Md. Aminul Islam, SO, OFRD, BARI | 4. Sumaiya Haque Omy, SO, Plant Breeding Division, BARI
5. Mst. Salina Akter, SO, Plant Breeding Division, BARI | 5. Sadia Sabrina Alam, SO, Plant Breeding Division, BARI
6. Nasrin Sultana, SSO, SPARRSO, Bangladesh | 6. Khandakar Faisal Ibn Murad, SO, Irrigation and Water Management Division, BARI
7. Arindam Biswas, SO, BARI | 
8. Dr. Selim Ahmed, PSO, OFRD, BARI | 

## Slide 2
Exploring Multispectral and Thermal Sensors regarding its application in Agricultural Monitoring System
Multispectral Broadband in Remote Sensing:
Multispectral remote sensing is the collection and analysis of the reflected, emitted, or back-scattered energy from an object or an area of interest in multiple bands of regions of the electromagnetic spectrum (Jensen, 2005).
The main purpose of multispectral imaging is the potential to classify the image using multispectral broad bands. Multispectral sensor captures image data within specific wavelength ranges across the electromagnetic spectrum.
Multispectral imagery usually have 3 to 10 different bands or more bands in each pixel of the images they produce. Each band has a descriptive titles. The examples of multispectral bands in the sensors typically include visible green, visible red, visible blue, near infrared, short-wave infrared, etc.
The wavelengths may be separated by filters or detected via the use of instruments that are sensitive to particular wavelengths, including light from frequencies beyond the visible light range, i.e. infrared and ultra-violet.

## Slide 3
List of Sensors (Multispectral Broadband)
Remote sensing systems gather data via instruments typically carried on satellites in orbit, drones, airborne platforms around the Earth. There are several multispectral remote sensing systems that can be categorized in the following way:
Multispectral imaging using discrete detectors and scanning mirrors
The European Space Agency (ESAs) Sentinel-2
Landsat Multispectral Scanner (MSS)
Landsat Thematic Mapper (TM)
Landsat 8 & 9 Operational Land Imager (OLI and OLI-2)
NOAA Geostationary Operational Environmental Satellite (GOES)
NOAA Advanced Very High Resolution Radiometer (AVHRR)
NASA and ORBIMAGE, Inc., Sea-viewing Wide field-of-view Sensor (SeaWiFS)
Daedalus, Inc., Aircraft Multispectral Scanner (AMS)
NASA Airborne Terrestrial Applications Sensor (ATLAS)
Multispectral imaging using linear arrays
SPOT 1, 2, and 3 High Resolution Visible (HRV) sensors and Spot 4 and 5 High Resolution Visible Infrared (HRVIR) and vegetation sensor
Indian Remote Sensing System (IRS) Linear Imaging Self-scanning Sensor (LISS)
Space Imaging, Inc. (IKONOS)
Digital Globe, Inc. (QuickBird)
ORBIMAGE, Inc. (OrbView-3)
ImageSat International, Inc. (EROS A1)
NASA Terra Advanced Spaceborne Thermal Emission and Reflection Radiometer (ASTER)
NASA Terra Multiangle Imaging Spectroradiometer (MISR)
Imaging spectrometry using linear and area arrays
NASA Jet Propulsion Laboratory Airborne Visible/Infrared Imaging Spectrometer (AVIRIS)
Compact Airborne Spectrographic Imager 3 (CASI 3)
NASA Terra/Aqua Moderate Resolution Imaging Spectrometer (MODIS)
NASA Earth Observer (EO-1) Advanced Land Imager (ALI), Hyperion, and LEISA Atmospheric Corrector (LAC)
Satellite analog and digital photographic systems
Russian SPIN-2 TK-350, and KVR-1000
NASA Space Shuttle and International Space Station Imagery

## Slide 4
Sensor Properties (Multispectral Broadband)
Sensor Name | Spatial | Spectral | Radiometric | Temporal | Data Source | Data Availability
Sentinel-2 | 10m/20m/60m | 13 Spectral bands with S2A: 443.9 nm-2202.4 nm and S2B: 442.3 nm-2185.7 nm spectrum | 8 to 16 bits | 5-day | https://scihub.copernicus.eu/dhus/#/home https://developers.google.com/earth-engine/datasets/catalog/COPERNICUS_S2_SR | 2015-Present Free of cost
Landsat | Pan-15m Vis-SWIR-30m | Nine spectral bands, including a pan band 430 nm to 2290 nm | 12 bit | 16-day | https://www.usgs.gov/core-science-systems/nli/landsat/landsat-data-access?qt-science_support_page_related_con=0#qt-science_support_page_related_con | 2013 – Present Free of cost
MODIS | 250 m (bands 1-2), 500 m (bands 3-7), 1km (bands 8-36) | 36 spectral bands (0.4-14.4 µm) Bands 1-19: 620-965 nm Bands 20-36: 3.660-14.385 µm | 12 bits | Daily, 8-day, 16-day, monthly, quarterly, yearly | https://lpdaacsvc.cr.usgs.gov/appeears/ http://earthdata.nasa.gov/ LANCE-MODIS ftp://ladsftp.nascom.nasa.gov/ ftp://n4ftl01u.ecs.nasa.gov/ | 01 Feb 2000 to December 2025 Free of cost (Most of the data are available in Hierarchical Data Format)
Hierarchical Data Format (HDF) is a set of file formats (HDF4, HDF5) designed to store and organize large amounts of data. Originally developed at the National Center for Supercomputing Applications, it is supported by The HDF Group, a non-profit corporation whose mission is to ensure continued development of HDF5 technologies and the continued accessibility of data stored in HDF.

## Slide 5
Sensor Properties (Multispectral Broadband)
Sensor Name | Spatial | Spectral | Radiometric | Temporal | Data Source | Data Availability
QuickBird | 0.65m/2.62m | Panchromatic with 1 band: 450-900 nm Multispectral with 4 bands: Blue: 450-520 nm Green: 520-600 nm Red: 630-690 nm Near IR: 760-900 nm | 11 bits | 1-3.5 days | 1. QuickBird Satellite Sensor ¦ Satellite Imaging Corp (satimagingcorp.com) 2.https://en.wikipedia.org/w/index.php?title=QuickBird&oldid=1048305413 | 2001-2015 Commercial
SPOT | Panchromatic: 1.5 m Multi-spectral: 6 m | 5 spectral bands Panchromatic: 450 – 745 nm Blue: 450–525 nm, Green: 530–590 nm, Red: 625–695 nm, NIR: 760–890 nm | 12 bits | 1-4 days | https://www.intelligence-airbusds.com/en/4871-ordering https://earth.esa.int/eogateway | SPOT: 1986 – Present SPOT 6&7: 2014-present

## Slide 6
Sentinel-2
1. Level-0 is compressed raw data. 2. Level-1A is uncompressed raw data with spectral bands. 3. Level-1B data is radiometrically corrected radiance data. 4. Level-1C product provides orthorectified Top-Of-Atmosphere (TOA) reflectance, with sub-pixel multispectral registration. 5. Level-2A product provides orthorectified Bottom-Of-Atmosphere (BOA) reflectance, with sub-pixel multispectral registration. N. B. Level-1C and Level-2A products are made available to users
The acquisition, processing, archiving and dissemination of Level-0 to Level-2A data can be performed by the Sentinel-2 Ground Segment. Level-2A can be also performed by the user using the Sentinel-2 Toolbox.
From Level-2A products Radiometric corrections may need in a multi-temporal approach (change detection). Cloud masking with QA60 band if needed Mosaic tiles Resample all bands to 10 m Spatial and bands subset Save image as geotiff for further analysis.
Pre-processing of Sensor imagery (Multispectral Broadband)

## Slide 7
Landsat
Pre processing techniques of all the sensors are almost similar. Level-2 Science Products are time-series observational data of sufficient length, consistency, and continuity to record effects of climate change, and serve as input into Landsat Level-3 Science Products. Level-3 science products represent biophysical properties of the Earth's surface
Radiometrical pre-processing-elimination of striping Geometrical mosaicking and rectification-fit the coordinate system of the map Image resampling by pixel doubling Relative calibration of detector data Combination of panchromatic and THEMATIC MAPPER data band replacement, principle component analysis, arithmetic terms, edge integration, color transformation.
Pre-processing of Sensor imagery (Multispectral Broadband)
MODIS
Modis data are transferred from the spacecraft to the ground station via Tracking and Data Relay Satellite System. The data are then sent to the Earth Observing System (EOS) data and Operating system (EDOS). The Level 1A, Level 1B, geolocation and cloud mask products and the high level MODIS land and atmosphere products are produced by the MODIS Adaptive Processing System, and then the data are parceled out.

## Slide 8
QuickBird
QuickBird offers satellite images in three basic products Basic ( corrections for elimination of the radiometric and sensor distortion are made) Standard (corrected with radiometric, sensor, and platform-induced distortions and the topographic distortion, using the GTOPO30 digital elevation model. The image is georeferenced and is made in a pre-set cartographic projection) and Orthorectified (corrected for radiometric, sensor and topographic distortion.).
counteracting atmospheric influences, input parameters are either taken from the recording conditions (e.g. sun and satellite angles, date, mean terrain height) or estimated by the implemented tool Spectra (atmosphere type, aerosol type, scene visibility). Orographic effects are modelled using a digital elevation model (DEM) ERDAS Imagine includes orographic correction.
QuickBird offers satellite images in three basic products Basic ( corrections for elimination of the radiometric and sensor distortion are made) Standard (corrected with radiometric, sensor, and platform-induced distortions and the topographic distortion, using the GTOPO30 digital elevation model. The image is georeferenced and is made in a pre-set cartographic projection) and Orthorectified (corrected for radiometric, sensor and topographic distortion.).
From Standard products Atmospheric corrections (ATCOR, Richter 1996, tool for an interactive atm. correction ) Correction orographic influences Need for homogeneous image mosaic.
Pre-processing of Sensor imagery (Multispectral Broadband)

## Slide 9
SPOT
1. Level-0 is compressed raw data.
2. Level 1A: Radiometric correction of distortions due to differences in sensitivity of the elementary detectors of the viewing instrument. Intended for users who wish to do their own geometric image processing.
3. Level 1B: Radiometric correction identical to that of level 1A. Geometric correction of systematic effects (panoramic effect, Earth curvature and rotation). Internal distortions of the image are corrected for measuring distances, angles and surface areas. Specially designed product for photo-interpreting and thematic studies.
4. Level 2A: Radiometric correction identical to that of level 1A. Geometrical correction done in a standard cartographic projection (UTM WGS84 by default) not tied to ground control points. Allowing for possible differences in location, this product is used to combine the image with geographical information of various types (vectors, raster maps and other satellite images).
5. Level 3 (Ortho): Map projection based on ground control points and a DEM based on Reference3D data to eliminate distortions due to relief.
Pre-processing of Sensor imagery (Multispectral Broadband)

## Slide 10
Steps for extracting information from the satellite image(s)
Identification of problem(s) need to be resolved using remotely sensed data.
Selection of appropriate sensor outputs to achieve the goals.
Identification of sensor band properties which are sensitive to respective target objects.
Image supervised/unsupervised classification using different machine learning algorithms (RF, ANN, DT, etc.), regression, image segmentation, clustering, etc.
Evaluation of classification/regression outcomes with respect to referenced datasets.

## Slide 11
Application of Sensors in Agricultural Monitoring
Sensor Name | Application
Sentinel-2 | Crop type identification (Luo et al. 2021; Gumma et al. 2020; Jiang et al. 2020), identification of cropping patterns (Chavan et al. 2020; Minh et al. 2019), monitoring crop growth stages (Ramadhani et al. 2020; Minh et al. 2019), yield prediction (Parida, Kumar, and Ranjan, 2021; Gomez et al. 2019), application in precision agriculture (Segarra et al. 2020), crop phenology analysis (Veloso et al. 2017) etc.
Landsat | NDVI time series for crop phenology mapping (Salik A. W. et al. 2019), analysis of cropping patterns (Fujihara Y. et al., 2020), plant area index for monitoring crop growth dynamics (Shang et a., 2014), identification of growth stage of sugarcane crop (kaur et al., 2017), estimating Fractional Vegetation Cover (X. Wang et al., 2017), crop condition and yield simulations (P. C. Doriaswami et. Al., 2004), estimating crop biomass using leaf area index (T. Dong et. Al., 2020), field-level crop yield mapping (Y. Kang et al., 2019)
MODIS | Vegetation and ecosystem dynamics, NDVI, Evapotranspiration, vegetation greenness
QuickBird | Agricultural Field Detection (Mustafa Turker et.al. 2021)crop identification and area estimation (Chenghai Yang et al. , 2007); crop yield estimation (GangPan et.al, 2009) mapping tree cover (G.S.Boggs et al. , 2010); object-based image analysis (Lübker T et al. , 2006); update and the revision of digital map and thematic map (Joon-Mook Kang et al. , 2008); updating cadastral information (A. Alexandrov et al. ); fuel load estimation (Jin et al. , 2012) ; archaeological applications (Antonio Lanorte et.al,
Spot | Landuse mapping (de Bie et. al. 2011), cropland mapping (Mohammed et al. 2020), crop identification (Yang et al. 2011), identification of crop parameters (Fiezul et al. 2013), plant nutrient status estimation (Muradyan et al. 2020), cover crop adoption (Hively et al. 2015), global food security analysis (Rembold et. al. 2019), detecting surface water content in crop plots (Benabdelouahab et al. 2015),

## Slide 12
Application of Sensors in Agricultural Monitoring
Sensor: MODIS (Moderate Resolution Imagine Spectroradiometer)
 | Collection | Keyword | Spatial resolution | Temporal resolution
MODIS/Terra + Aqua Land cover dynamics yearly L3 Global 500 m SIN grid | Combined MODIS | Phenology and vegetation indices | 500 m | Yearly
MODIS/Terra + Aqua Leaf Area Index/FPAR 8-day L4 Global 500 m SIN grid | Combined MODIS | Fraction of Photosynthetically Active Radiation (FPAR), Leaf Area Index (LAI) | 500 m | Multi-Day
MODIS/Terra + Aqua Photosynthetically Active Radiation Daily 3-hour L3 Global 5 km SIN grid | Combined MODIS | Photosynthetically Active Radiation (PAR) | 5600.0 m | < Daily
MODIS/Terra + Aqua Photosynthetically Active Radiation Daily/3-hour L3 Global 1 km SIN grid | Combined MODIS | Photosynthetically Active Radiation (PAR) | 1000.0 m | < Daily
MODIS/Terra + Aqua Photosynthetically Active Radiation Daily 3-hour L3 Global 0.05 deg CMG | Combined MODIS | Photosynthetically Active Radiation (PAR) | 5600.0 m | < Daily

## Slide 13
13
Application of Sensors in Agricultural Monitoring
Sensor: Sentinel-2
Band Number | Keyword | Spatial resolution (m) | Temporal resolution (days) | Reference
B05, B06, B07 | Crop production estimation | 10-20 | 10 (5 days at equator) | Karlson et al. 2020
B11 B12 | Crop production estimation | 10-20 | 10 (5 days at equator) | Karlson et al. 2020
B2, 3, 4 and 8 | Crop type identification and cropping systems | 10 | 10 | Gumma et al. 2020, Ibrahim et al. 2021
B3, 4, 5, 6,7, 8,8a | Phenological stages, yield estimation | 10 | 10 | Omer Gokberk Narin & Saygin Abdikan (2020), Boori et al. 2020

## Slide 14
Band Number | Band Name | Keyword | Spatial resolution | Temporal resolution
B01 | Coastal aerosol | Aerosol scattering | 60 | 10
B02 | Blue | Blue | 10 | 10
B03 | Green | Green | 10 | 10
B04 | Red | Red | 10 | 10
B05 | Rededge 1 | Vegetation Classification | 20 | 10
B06 | Rededge 2 | Vegetation Classification | 20 | 10
B07 | Rededge 3 | Vegetation Classification | 20 | 10
B08 | NIRwide | Sensitive to chlorophyll, biomass and protein | 10 | 10
B08a | NIRnarrow | Vegetation Classification | 20 | 10
B09 | Water Vapor | Water vapor absorption | 60 | 10
B010 | SWIR Cirrus | Detection of thin cirrus | 60 | 10
B11 | SWIR 1 | Sensitive to lignin, starch and forest above ground biomass | 20 | 10
B12 | SWIR 2 | Distinction of live biomass, dead biomass and soil | 20 | 10
Bolyn et al. 2018, Sanchez et al. 2020

## Slide 16: Thanks