## Slide 1
1
Application of Sensors in Agricultural Monitoring
Sensor: Sentinel-2
Band Number | Keyword | Spatial resolution (m) | Temporal resolution (days) | Reference
B05, B06, B07 | Crop production estimation | 10-20 | 10 (5 days at equator) | Karlson et al. 2020
B11 B12 | Crop production estimation | 10-20 | 10 (5 days at equator) | Karlson et al. 2020
B2, 3, 4 and 8 | Crop type identification and cropping systems | 10 | 10 | Gumma et al. 2020, Ibrahim et al. 2021
B3, 4, 5, 6,7, 8,8a | Phenological stages, yield estimation | 10 | 10 | Omer Gokberk Narin & Saygin Abdikan (2020), Boori et al. 2020

## Slide 2
Band Number | Band Name | Keyword | Spatial resolution | Temporal resolution
B01 | Coastal aerosol | Aerosol scattering | 60 | 10
B02 | Blue | Blue | 10 | 10
B03 | Green | Green | 10 | 10
B04 | Red | Red | 10 | 10
B05 | Rededge 1 | Vegetation Classification | 20 | 10
B06 | Rededge 2 | Vegetation Classification | 20 | 10
B07 | Rededge 3 | Vegetation Classification | 20 | 10
B08 | NIRwide | Sensitive to chlorophyll, biomass and protein | 10 | 10
B08a | NIRnarrow | Vegetation Classification | 20 | 10
B09 | Water Vapor | Water vapor absorption | 60 | 10
B010 | SWIR Cirrus | Detection of thin cirrus | 60 | 10
B11 | SWIR 1 | Sensitive to lignin, starch and forest above ground biomass | 20 | 10
B12 | SWIR 2 | Distinction of live biomass, dead biomass and soil | 20 | 10
Bolyn et al. 2018, Sanchez et al. 2020